## Slide 1: Indio Subbasin Alternative Plan Update Annual Report for Water Year 2024-2025
Public Workshop
March 11, 2026

## Slide 2: Teams – Quick How To
Your screen should look like this:
Turn on/off your Mic (mute) and Camera (video) using the controls along the bottom
You may need to wiggle your mouse to make the controls appear
For Callers: use *6 to unmute on the phone

## Slide 3: Teams – How to Ask a Question
Our organizer will mute everyone at the beginning of the meeting
Let us know you have a question by
  Raising your hand (bottom of screen)
  Entering the Chat (bottom of screen)
    Click on the right panel, type your message and hit SEND
Once we receive your request, we will call on you and answer your question
For Callers: when asked for questions or comments, use *6 to unmute

## Slide 4: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 5: Indio Subbasin Team
Project Consultants
  Todd Groundwater
Indio Subbasin Groundwater Sustainability Agencies (GSAs)
  Coachella Valley Water District
  Coachella Water Authority
  Desert Water Agency
  Indio Water Authority
`

## Slide 6: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 7: Indio Subbasin Annual Report for WY 2023-2024
Annual Report is required by Sustainable Groundwater Management Act (SGMA)
  General information
  Subbasin conditions
  Implementation progress of projects and management actions (PMAs)
9th Annual Report (5th report following submittal of Indio Subbasin 2022 Alternative Plan Update)
  Covers WY 2024-2025 (Oct. 1, 2024 – Sept. 30, 2025)
Will be submitted to DWR by April 1, 2026

## Slide 9: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 10: Groundwater Elevation Data
Groundwater elevations from 355 wells were used to develop contour maps and change in storage maps
2022 Plan Update identified 57 Key Wells to track groundwater sustainability
  Each well has a minimum threshold (MT—set at recent observed lowest elevation)
  Current groundwater elevations were compared to the MTs
    Levels in all wells were above the MT
    Hydrographs of each of these wells are included in the report as an Appendix

## Slide 12
Questions?

## Slide 13: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 14: Groundwater Extractions
Groundwater extractions are metered for most uses except
  Minimal pumpers
  Tribal trust lands
272,629 AF
Groundwater pumping increased 2 percent from last water year
Water Use Sector | Groundwater Extractions (AF) | Method of Measurement | Accuracy of Measurement
Agriculture1 | 32,773 | 100% metered | ±2%
Industrial2 | 888 | 100% metered | ±2%
 |  | 0% estimated | ±50%
Urban3 | 237,468 | 99% metered | ±2%
 |  | 1% estimated | ±50%
Undetermined4 | 1,500 | 100% estimated | ±50%
Total Production | 272,629 |  | 

## Slide 15
Questions?

## Slide 16: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 17: Multiple Water Sources
Capture and recharge of Whitewater River stormflows began in 1918
Coachella Canal completed in 1949
CVWD and DWA contract for State Water Project (SWP) water in 1963
  Recharge at Whitewater River Groundwater Replenishment Facility (GRF) begins in 1973
Water recycling began in 1965
Coachella Canal construction
Whitewater River GRF
17

## Slide 18: Local Surface Water
DWA stream diversions
  Snow, Falls, and Chino Creeks
465 AF surface water use in DWA’s service area
  49% agriculture
  51% urban
WY 2024-2025 Direct Use of Local Surface Water in the Indio Subbasin
Snow Creek
Water Use Sector | Surface Water Use (AF) | Method of Measurement | Accuracy of Measurement
Agriculture1 | 228 | 100% metered | ±2%
Industrial | 0 | Not applicable | --
Urban1 | 237 | 100% metered | ±2%
Total Surface Water Use | 465 |  | 

## Slide 19: Imported Water – Direct Use
CVWD receives Colorado River water from Coachella Canal
279,852 AF imported water for direct use in Plan Area
  85% agriculture
  15% urban
2 percent increase from last year
Coachella Canal
WY 2024-2025 Imported Water for Direct Use in Plan Area
Water Use Sector | Water Source | Imported Water Use (AF) | Method of Measurement | Accuracy of Measurement
Agriculture1 | Coachella Canal | 246,855 | 100% metered | ±2%
Urban2 | Coachella Canal | 32,997 | 100% metered | ±2%
Industrial | Coachella Canal | 0 | 100% metered | ±2%
Environmental3 | Coachella Canal | 0 | Not applicable | --
Total Imported Water for Direct Use4 |  | 279,852 |  | 

## Slide 20: Imported Water – Groundwater Replenishment
Two sources of water used for replenishment:
  DWA and CVWD receive State Water Project exchange water from Colorado River Aqueduct (CRA)
  CVWD receives Colorado River water from Coachella Canal
265,471 AF imported water for replenishment
  10 percent less than WY2024
WY 2024-2025 Imported Water for Replenishment in Plan Area
WWR-GRF
Water Use Sector | Water Source | Imported Water Use (AF) | Method of Measurement
Groundwater Replenishment | Coachella Canal6 | 12,932 | 100% metered
Groundwater Replenishment | SWP Exchange/CRA | 252,539 | 100% metered
Total Imported Water for Groundwater Replenishment |  | 265,471 | 
Notes: SWP exchange water is recharged at the WWR-GRF

## Slide 21: Imported Water – Groundwater Replenishment
267,370 AF water for replenishment
  10,164 AF at Palm Desert GRF
  2,768 AF at Thomas E. Levy GRF
  254,438 AF at Whitewater River GRF
    Includes local surface water
WY 2024-2025 Total Groundwater Replenishment
PD-GRF
Replenishment Facility | Water Source | Volume Recharged in WY 2025 (AF)
Whitewater – GRF | Imported Water | 252,539
 | Local Surface Water | 1,899
Palm Desert – GRF | Imported Water | 10,164
TEL – GRF | Imported Water | 2,768
Total |  | 267,370
10 percent decrease over last year
Notes: SWP exchange water is recharged at the WWR-GRF

## Slide 22: Recycled Water
Three water reclamation plants (WRPs) provide recycled water
  Palm Springs WWTP/DWA WRP
  CVWD WRP-7
  CVWD WRP-10
13,164 AF recycled water produced
  100% urban
WY 2023-2024 Recycled Water Use in the Indio Subbasin
DWA WRP
Water Use Sector | Water Source | Recycled Water Use (AF) | Method of Measurement | Accuracy of Measurement
Urban1 | DWA WRP | 3,122 | 100% metered | ±2%
Urban1 | CVWD WRP 7 | 2,055 | 100% metered | ±2%
Urban1 | CVWD WRP 10 | 7,987 | 100% metered | ±2%
Total Recycled Water Use |  | 13,164 |  | 
Notes: 6 percent increase

## Slide 23
Questions?

## Slide 24: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 25: Total Water Use
WY 2024-2025 Water Demand and Supply – Plan Area
Notes: SWP exchange water is recharged at the WWR-GRF

## Slide 26: Total Water Use
Total Water Demand Actual and Forecasted – Plan Area
Notes: SWP exchange water is recharged at the WWR-GRF

## Slide 27
Questions?

## Slide 28: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 29: Change in Groundwater Storage
Comparison of Inflows and Outflows
Inflows
  Replenishment
  WW Percolation
  Return Flows
  Subsurface Flow
  Natural Infiltration
Outflows
  Evapotranspiration (ET)
  Drains
  Pumping
  Subsurface Flow

## Slide 30: Change in Groundwater Storage
Annual change in storage
  +137,052 AF
Average change in storage
  Since 2009, 10-year average (yellow line) is positive and the 20-year average (green line) since WY 2023
  Shows the Indio Subbasin is still sustainable
W = Wet, A = Above Normal, B = Below Normal, D = Dry, C = Critically Dry

## Slide 31: Change in Groundwater Levels
Maps show change in groundwater levels
  One year change (next slide)
  Long-term change since 2009 historical lows (following slide)
Change in groundwater levels is a proxy for change in storage
Based on measured water levels at 356 wells throughout the Indio Subbasin

## Slide 32: One Year Change
Groundwater levels generally increased in the past water year
  Increases near WWR-GRF but declines downstream due to variability in recharge
  Declines in the middle part of the Subbasin due to less TEL recharge
WY 2024 to WY 2025

## Slide 33: Long-Term Change
Basin-wide increases since 2009 historical lows
Water levels have increased or stabilized
Very localized declines in Mid-Valley area
WY 2009 to WY 2025

## Slide 34
Questions?

## Slide 35: Agenda
Welcome and Introductions
Annual Report Status
Groundwater Elevation Data
Groundwater Extractions
Surface Water
Total Water Use
Change in Groundwater Storage
Plan Implementation Progress
Public Comment

## Slide 36: Projects & Management Actions
1: Urban Water Conservation
2: Golf Water Conservation
3: Agricultural Water Conservation
4: Increased Surface Water Diversion
5: Delta Conveyance Facility
6: Lake Perris Seepage
7: Sites Reservoir
8: Future Supplemental Water Acquisitions
9: EVRA Potable Reuse
10: Mid-Valley Pipeline Direct Customers
11: East Golf Expansion
12: Oasis Distribution System
13: WRP-10 Recycled Water Delivery
14: WRP-10 Tertiary Expansion
15: Canal Water Pump Station Upgrade
16: WRP-7 Recycled Water Delivery
17: WRP-4 Tertiary Expansion & Delivery
18: DWA WRP Recycled Water Delivery
19: PD-GRF Phase 2 Expansion
20: TEL-GRF Expansion
21: WWR-GRF Operation
22: Eliminate Wastewater Percolation
23: Wellhead Treatment
24: Small Water System Consolidations
25: Septic to Sewer Conversions
26: CV-SNMP GW Monitoring Program Workplan
27: CV-SNMP Development Workplan
28: Colorado River Salinity Forum
29: Source Water Protection
Water Supply Development
Source Substitution & Replenishment
Water Quality Protection
Water Conservation

## Slide 37: 2027 Alternative Plan Update
SGMA Plans are required to be evaluated every five years
Indio Subbasin has decided to prepare a stand alone update to the 2022 Alternative Plan
Development is underway
  Updated demand forecasts
  Updated supply forecasts
    Climate change
  Updated groundwater model
    Extended to the San Gorgonio Subbasin boundary
  New scenarios to simulate future groundwater management

## Slide 38
Questions?

## Slide 39: Public Comment
Input and feedback are welcomed
For Callers – you may need to press *6 to unmute

## Slide 40: Next Steps
WY 2025 Annual Report can be downloaded:
Indio Subbasin Annual Report for WY 2024-2025 Council/Board Presentation
  Coachella Valley Water District – TBD
  Coachella Water Authority – TBD
  Desert Water Agency – TBD
  Indio Water Authority – TBD
www.IndioSubbasinSGMA.org

## Slide 41: Stay Involved – Visit our Website
www.IndioSubbasinSGMA.org